## Slide 1: Water Supply Reliability Estimation: an overview
Jay R. Lund
Director, Center for Watershed Sciences
Professor of Civil and Environmental Engineering
University of California, Davis
watershed.ucdavis.edu/shed/lund/
CaliforniaWaterBlog.com

## Slide 2: Outline
2
Water System Portfolios
Water demands
Sources of unreliability
Estimating Reliability
Metrics of Reliability
Lessons

## Slide 3: How we know our water supplies are mostly reliable.
3

## Slide 4: Complexity of Water in California

## Slide 5: Sacramento Valley Precipitation
5
2014:
8th driest in 106 years,
4th driest in runoff
2016-17
1982-83
2015-16
1976-77
2013-14
2014-15
2010-11
2015-16

## Slide 6: Most annual rainfall variability in US
SOURCE: Michael Dettinger, 2011. “Climate Change, Atmospheric Rivers, and Floods in California—A Multimodel Analysis of Storm Frequency and Magnitude Changes.” Journal of the American Water Resources Association 47(3):514-523.
NOTES: Dots represent the coefficient of variation of total annual precipitation at weather stations for 1951-2008, Larger values have greater year-to-year variability.
Annual coefficient of variation

## Slide 7
Natural Runoff Variation
Source: California DWR
Unimpaired Delta Outflow

## Slide 8: Water Systems
8
Simple: Simplified:
Urban
Farms
Fish
Surface water
Groundwater
Water imports and exports

## Slide 9: Water Systems
9
Orange County:

## Slide 10
3
Water supply system portfolio actions
Water supply | 
Water Source availability | Treatment
Capture of fog, precipitation, streams, groundwater, wastewater | Existing water and wastewater treatment
Protection of source water quality | New water and wastewater treatment
Conveyance capacities | Wastewater reuse
Canals, pipelines, aquifers, tankers (sea or land), bottles, etc. | Ocean Desalination
 | Contaminated aquifers
Storage capacities | Operations
Surface reservoirs, aquifers and recharge, tanks, snowpack, etc. | Reoperation of storage and conveyance
 | Conjunctive use
Water demands and allocation | 
Agricultural use efficiencies and reductions | Ecosystem demand management
Urban water use efficiencies and reductions | Recreation water use efficiencies
Incentives to work well together | 
Pricing | Subsidies, taxes
Markets | Education
“Norming”, shaming | 

## Slide 11: San Diego water supply portfolio
11
588 taf/yr
578 taf/yr
477 taf/yr
694 taf/yr

## Slide 12: Local and Statewide Portfolio
Local Activities:
- Conservation and use efficiency
- Wastewater reuse
- Desalination (brackish & ocean)
- Groundwater use and recharge
- Surface reservoir operations
- Water markets and exchanges
Statewide Activities:
- Inter-regional water conveyance
- Surface reservoir operations
- Plumbing codes & conservation incentives
- Groundwater banking and recharge
- Water market support and conveyance
- Wastewater reuse subsidies
Integrating mix of actions – portfolio planning.

## Slide 13: Water Demands
13
Many types of water demands/uses
  Urban – landscaping, sanitation, drinking, etc.
  Agriculture – trees, vegetables, pasture, etc.
  Environmental – water quality/dilution, habitat, ecosystem support, etc.
Demands vary with time (hour, season, historical)
Uses and shortages are not all equally valued

## Slide 14: Two Views of Water Demands
14
Point demands Value/demand curves
Point demand volume
Time of year
Use A
Use E
Use U
Total Value of delivery
Volume delivered to use at time t
Use A
Use E
Use U
Consequences of “shortage”
“There is a shortage of sport cars – I don’t have one.”
“There is rarely a shortage of water, but often a shortage of cheap water.”

## Slide 16: Sources of Unreliability
16
Lack of inflow, drought
Flood
Earthquakes, wildfires, etc.
Mechanical and operational failures (Flint)
Water demands
Regulations
Unreliable rules or agreements
Multiple failures

## Slide 17: Representing Sources of Unreliability
17
Events, time series, or probabilities
Based on:
  Historical experiences
  Scenarios of concern
  Synthetic cases
Use many time series – Monte Carlo types of analysis

## Slide 18: System Simulation Models
18
Simple system:
Urban
Farms
Fish
Surface water
Groundwater
Water imports and exports
Model inputs:
  Capacities
  Inflows
  Water demands
  Operating rules
Model outputs:
  Deliveries
  Storages
  Losses
Time-step simulation:
Rules and capacities
Conservation of mass

## Slide 19: Estimating System Reliability
19
Simulation modeling (“What if?” modeling)
Representing/simplifying legions of details, capacities, and responses
Running simulation for each case to estimate responses and consequences
Assigning probabilities
Assess overall reliabilities and consequences

## Slide 20: Model Results to Reliabilities
20
Delivery-reliability for a “level of development”
from DWR data 2015
Time-series of model results
Probabilities of results

## Slide 21: Seasonal Operation Reliabilities
21
Reliability by “Position Analysis”
Today’s storage
Forecast demands
Many future inflows
Probabilities of storage or delivery results
from Hirsch 1978
Minimum storage in millions of gallons
from Murk 1995

## Slide 22: Estimating System Reliability
22
“All models are wrong, but some are useful.”
Delivery reliability models and results
Importance of model interpretation
from DWR data 2015

## Slide 23: Modeling “Errors” Unavoidable
23
“All models are wrong, but some are useful.” G.E.P. Box 1978
“The purpose of computing is insight, not numbers.” R. Hamming 1962
Model components:
Model software (formulation, calibration, version)
Input data (hydrology, demands, operating rules)
Modeler (orchestration + interpretation)
Interpretation and documentation fundamental.

## Slide 24: SWP Delivery Capabilities Reports
24
from DWR 2018
Estimates SWP delivery capabilities overall and for individual contractors for historical hydrology and present conditions - updated every 2 years

## Slide 25: Orange County
25
From OCMWD 2016
Complex local & regional system
Multiple supplies raise reliability
Climate and Waterfix matter

## Slide 26: MWD’s Integrated Resources Plan
26
Modeling integrates diverse knowledge
As a wholesaler, demands are important to their reliability
Prefer >1 maf in storage

## Slide 27: Reliability in a Portfolio of Actions
27
Agricultural example:
Surplus to bank, sell, or exchange
Pump more groundwater
Fallow annual crops
Purchase water for trees
Delivery target
Surface water delivery

## Slide 28: Metrics of Reliability
28
Many metrics proposed and used for different purposes
“Firm Yield” – 100% modelled reliability for historical inflow record
Reliability for delivery target volume
Robustness, resiliency, vulnerability
Expected annual damage
Probability distributions of performance

## Slide 29: Climate change and reliability
29
More seasonal and inter-annual variability in surface water supplies – groundwater more important
from DWR data 2015

## Slide 30: Many Forms of “Non-Stationarity”
Climate
  Sea level rise
  Warming
  Precipitation change
  Extreme whiplash
Deterioration
  Aging infrastructure
  Contaminants – salts, nitrates, etc.
  Mining legacy
  Groundwater overdraft
  Earthquakes
  Sacramento-San Joaquin Delta
Water demands
  Crop commodity prices
  Conservation actions
  Population growth and urbanization
Ecosystems
  New invasive species
  Continued degradation
Science and technology
  New chemicals
  New technologies
Management
  Regulations
  Agreements
  Funding
  Storage operations
  Infrastructure capacities

## Slide 31: Some Issues and Lessons
31
Reliability estimates integrate knowledge of system, demands, supplies, and operations
Reliability of components vs. reliability of system (Delta reliability vs. system reliability)
Portfolio reliability & management are key
Model results have both insights and “errors”
Importance of interpretation and insights
Non-stationarity has many forms
Demand interpreted delivery-reliability plots!

## Slide 32: Suggested Readings
Hazen, A. (1914), “Storage to be provided in impounding reservoirs for municipal water supply,” Transactions ASCE, Vol. 77, pp. 1539-1669.
Hirsch, R.M. (1978), Risk Analyses for A Water-Supply System … , Open File Report 78-452, USGS
Kuria, F., Vogel, R.M., Uncertainty Analysis for Water Supply Reservoir Yields, J. of Hydrology, 2015.
DWR, State Water Project Delivery Capability Report 2015.
MWDSC, Technical Appendix, Integrated Water Resources Plan Update 2015
MWDOC, Orange County Water Reliability Study, December 2016
Lund, J. "California’s Agric. & Urban Water Supply Reliability and the Sacramento–San Joaquin Delta," SFEWS, October 2016.

## Slide 33: Is this true for us?
33
Richard Hamming, 1968
“Indeed, one of my major complaints about the computer field is that whereas Newton could say, "If I have seen a little farther than others, it is because I have stood on the shoulders of giants," I am forced to say, "Today we stand on each other's feet."
Perhaps the central problem we face in all of computer science is how we are to get to the situation where we build on top of the work of others rather than redoing so much of it in a trivially different way. Science is supposed to be cumulative, not almost endless duplication of the same kind of things.”